## Slide 1
KubeEdgeInfer
A Closed-Loop, eBPF-Driven Kubernetes Framework for Heterogeneous
Distributed LLM Inference on Consumer Edge Clusters
Your Name
Department of ________
Guide: Sir's Name
Date
1 / 10
Notes: Fill in your name, department, guide and date before presenting.

## Slide 2
Introduction
•
Large Language Models (LLMs) are often too large to fit on a single consumer GPU.
•
Pipeline parallelism solves this by splitting model layers across several machines, forming an inference assembly line.
•
Existing frameworks are built either for stable datacenter interconnects, or they split layers statically and never revisit that decision.
•
Consumer and edge hardware is inherently heterogeneous: different GPU generations, WiFi rather than Ethernet, and thermal variance under sustained load.
Core Idea
Continuously observe real hardware conditions at the kernel level, and let the model's layer partition adapt to them instead of staying fixed.
2 / 10

## Slide 3
Literature Review
Work
Year
Contribution
Gap this work addresses
EdgeShard
2024
DP device selection and layer partition
Profiled offline; plan never revisited
Galaxy
2024
Tensor/sequence parallelism with overlap
One-shot planning, no adaptation
Helix
2025
Max-flow MILP over mixed GPUs
Solver too heavy for a live loop
TPI-LLM
2024
Memory scheduling for 70B on small RAM
Optimises memory, not degradation
prima.cpp
2025
CPU/GPU co-scheduling on home clusters
Schedule fixed at load time
Head-level split
2025
Attention-head granularity, with migration
Triggered by memory pressure only
Parallax
2025
Serving over volunteer machines
No kernel-level measurement
Adaptive split (MBRL)
2025
Learns the split point as the channel varies
Needs training; no optimality proof
Distributed LLM survey
2025
Surveys the field
Names adaptation as an open problem
sched_ext (eBPF)
2025
Linux schedulers loaded as eBPF programs
Single host; no model pipeline
Common limitation
Every one of these measures the hardware before the run, and never measures again.
3 / 10

## Slide 4
Problem Statement
Static partitioning ignores real-time hardware variability.
Thermal Throttling
GPUs slow down mid-inference as they heat up under sustained load.
Network Latency
WiFi and edge links have variable latency — no InfiniBand or NVLink at home.
Node Failure
A laptop closes its lid or drops off the network, and its layers go with it.
Consequence: Pipeline Bubble Time
Fast machines sit idle waiting on slower ones. A one-time, fixed split cannot correct itself as conditions change.
4 / 10

## Slide 5
Objectives and Contributions
1
Capture system telemetry — network transfer latency, GPU thermal state, throttling — using eBPF and NVML, with no change to the model code.
2
Design a dynamic partitioning algorithm that computes the optimal contiguous layer split from live telemetry, and prove it optimal for each snapshot.
3
Integrate telemetry and partitioning decisions directly into a Kubernetes control loop, applying them without restarting pods.
4
Enable autonomous healing: automatic re-partitioning on node failure or sustained thermal throttling.
5
Stabilise the loop with hysteresis — a 15% improvement threshold and a 30 s cooldown — so noisy telemetry cannot cause thrashing.
6
Evaluate bubble time, throughput and time-to-first-token empirically against static partitioning and an offline-profiling baseline.
5 / 10

## Slide 6
Architecture — How It Works
1. WATCH
eBPF + NVML
Telemetry
2. DECIDE
DP Partitioning
Algorithm
3. ACT
Kubernetes
Controller
4. HEAL
Autonomous
Recovery
loop repeats continuously
•
Watch: kernel-level flow latency, GPU temperature, memory, throttle state.
•
Decide: compute the optimal contiguous split from live metrics.
•
Act: re-assign layers, reroute traffic, apply the new split with no restart.
•
Heal: detect node failure within 3 s, re-partition across the survivors.
6 / 10

## Slide 7
Results
Injected condition
KubeEdgeInfer
Profile-once
Static split
No fault
42 ms
42 ms
42 ms
Thermal throttle (0.4x)
52 ms
102 ms
102 ms
Network delay (80 ms)
62 ms
122 ms
122 ms
Thermal + network
62 ms
182 ms
182 ms
Node failure
62 ms
62 ms
pipeline stops
Bottleneck-stage cost per token; lower is better. 12 layers over 3 machines.
Headline
49% lower bottleneck cost under thermal throttling and under network degradation; 66% lower when both occur together. Under node failure the static split is undefined over the surviving set, so the pipeline stops — KubeEdgeInfer re-partitions and continues.
Reproducible with go run ./bench/dpsim; end-to-end throughput comes from bench/run.py, which needs a live cluster.
7 / 10

## Slide 8
Novelty
Feature
EdgeShard
Galaxy
Helix
prima.cpp
Ours
Heterogeneous edge support
✓
✓
✗
✓
✓
Kernel-level telemetry (eBPF)
✗
✗
✗
✗
✓
Dynamic re-partitioning
✗
✗
✗
✗
✓
Thermal awareness
✗
✗
✗
✗
✓
Autonomous healing
✗
✗
✓
✗
✓
Declarative K8s API
✗
✗
✗
✗
✓
One-line novelty statement
We turn a static, one-time model-splitting decision into a continuous, self-correcting one — driven by real kernel-level measurements instead of assumptions.
8 / 10

## Slide 9
Summary
•
First system to close the loop: eBPF/NVML telemetry → Kubernetes scheduling → self-healing, for edge LLM inference.
•
The partitioner is provably optimal for a fixed telemetry snapshot — it reduces to the classical linear partition problem, and is unit-tested against brute force on 200 random instances.
•
Adaptive behaviour is validated empirically through a staged ablation under simulated network, thermal and failure conditions.
•
Distributed GPT-2 output is token-identical to single-process inference, so adaptivity costs no correctness.
•
Fully software-based and reproducible — no proprietary hardware lab required.
Thank you — Questions?
9 / 10

## Slide 10
References
[1]
M. Zhang, J. Cao, X. Shen, Z. Cui. EdgeShard: Efficient LLM Inference via Collaborative Edge Computing. IEEE Internet of Things Journal, 2024. arXiv:2405.14371.
[2]
Galaxy: A Resource-Efficient Collaborative Edge AI System for In-situ Transformer Inference. IEEE INFOCOM, 2024. arXiv:2405.17245.
[3]
Helix: Serving Large Language Models over Heterogeneous GPUs and Network via Max-Flow. ACM ASPLOS, 2025. arXiv:2406.01566.
[4]
TPI-LLM: Serving 70B-scale LLMs Efficiently on Low-resource Edge Devices. 2024. arXiv:2410.00531.
[5]
Prima.cpp: Fast 30-70B LLM Inference on Heterogeneous and Low-Resource Home Clusters. 2025. arXiv:2504.08791.
[6]
Large Language Model Partitioning for Low-Latency Inference at the Edge. 2025. arXiv:2505.02533.
[7]
Parallax: Efficient LLM Inference Service over Decentralized Environment. 2025. arXiv:2509.26182.
[8]
Adaptive layer splitting for wireless large language model inference in edge computing. FITEE, Springer, 2025. doi:10.1631/FITEE.2400468.
[9]
Distributed LLMs and Multimodal Large Language Models: A Survey on Advances, Challenges, and Future Directions. 2025. arXiv:2503.16585.
[10]
Towards Agentic OS: An LLM Agent Framework for Linux Schedulers. 2025. arXiv:2509.01245.
Tools: cilium/ebpf (CO-RE loader), Kubernetes controller-runtime, NVIDIA NVML, k3s, Hugging Face Transformers.
10 / 10